## Slide 1: Lecture 2: Representing Integers
CS 105
Spring 2025

## Slide 2: Review: Memory
Memory is an array of bits
A byte is a unit of eight bits
An index into the array is an address, location, or pointer
  Often expressed in hexadecimal
We speak of the value in memory at an address
  The value may be a single byte …
  … or a multi-byte quantity starting at that address
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
0
0
1
1
1
0
1
0
0
1
1
0
0
1
1
1
0
0
1
2
3
01101100
01010011
11010001
00110111
bytes

## Slide 3: Review: Bits Require Interpretation
10001100 00001100 10101100 00000000
might be interpreted as
  The integer 3,485,745
  A floating point number close to 4.884569 x 10-39
  The string “105”
  A portion of an image or video
  An address in memory

## Slide 4: Representing Integers
Arabic Numerals: 47
Roman Numerals: XLVII
Brahmi Numerals:
Tally Marks: IIII IIII IIII IIII IIII IIII IIII IIII IIII II

## Slide 5: Base-10 Integers
1000 (103) | 100 (102) | 10 (101) | 1 (100)
0 | 0 | 0 | 5
0 | 0 | 4 | 7
1 | 8 | 8 | 7

## Slide 6: Base-2 Integers (aka Binary Numbers)
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 7: Exercise 1: Binary Numbers
Consider the following four-bit binary values. What is the (base-10) integer interpretation of these values?
  0001
  1010
  0111
  1111
1
10
7
15

## Slide 8: Representing Signed Integers
+/- | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
-
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: Issues: two zeros, arithmetic is different for pos vs neg (and weird around zero), e.g, try 5+1 vs -5+1 vs. -5 + 6

## Slide 9: Representing Signed Integers
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20) | -128
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: issue: zero no longer zero -> multiplication is weird

## Slide 10: Representing Signed Integers
-128 (-27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 11: Exercise 2: (Signed) Binary Numbers
Consider the following four-bit binary values. What is the (base-10) signed integer interpretation of these values?
  0001
  1010
  0111
  1111
1
-6
7
-1

## Slide 12: Signed Integer Trivia
Base-10 | unsigned | signed
7 | 111 | 
6 | 110 | 
5 | 101 | 
4 | 100 | 
3 | 011 | 011
2 | 010 | 010
1 | 001 | 001
0 | 000 | 000
-1 |  | 111
-2 |  | 110
-3 |  | 101
-4 |  | 100
For signed ints:
  high-order (left-most) bit is 0 for pos values, 1 for neg
  000…0 is 0
  111…1 is -1
  same representation as unsigned for numbers that can be represented with both
  ~x+1 == -1*x

## Slide 13: Integers in C
C Data Type | Size (bytes)
unsigned char | 1
unsigned short | 2
unsigned int | 4
unsigned long | 8
C Data Type | Size (bytes)
char | 1
short | 2
int | 4
long | 8
Notes: Note: unsigned demo

## Slide 14: ASCII characters
Char | Dec | Binary
! | 33 | 00100001
" | 34 | 00100010
# | 35 | 00100011
$ | 36 | 00100100
% | 37 | 00100101
& | 38 | 00100110
' | 39 | 00100111
( | 40 | 00101000
) | 41 | 00101001
* | 42 | 00101010
+ | 43 | 00101011
, | 44 | 00101100
- | 45 | 00101101
. | 46 | 00101110
/ | 47 | 00101111
0 | 48 | 00110000
Char | Dec | Binary
1 | 49 | 00110001
2 | 50 | 00110010
3 | 51 | 00110011
4 | 52 | 00110100
5 | 53 | 00110101
6 | 54 | 00110110
7 | 55 | 00110111
8 | 56 | 00111000
9 | 57 | 00111001
: | 58 | 00111010
; | 59 | 00111011
< | 60 | 00111100
= | 61 | 00111101
> | 62 | 00111110
? | 63 | 00111111
@ | 64 | 01000000
Char | Dec | Binary
A | 65 | 01000001
B | 66 | 01000010
C | 67 | 01000011
D | 68 | 01000100
E | 69 | 01000101
F | 70 | 01000110
G | 71 | 01000111
H | 72 | 01001000
I | 73 | 01001001
J | 74 | 01001010
K | 75 | 01001011
L | 76 | 01001100
M | 77 | 01001101
N | 78 | 01001110
O | 79 | 01001111
P | 80 | 01010000
Char | Dec | Binary
Q | 81 | 01010001
R | 82 | 01010010
S | 83 | 01010011
T | 84 | 01010100
U | 85 | 01010101
V | 86 | 01010110
W | 87 | 01010111
X | 88 | 01011000
Y | 89 | 01011001
Z | 90 | 01011010
[ | 91 | 01011011
\ | 92 | 01011100
] | 93 | 01011101
^ | 94 | 01011110
_ | 95 | 01011111
` | 96 | 01100000
Char | Dec | Binary
a | 97 | 01100001
b | 98 | 01100010
c | 99 | 01100011
d | 100 | 01100100
e | 101 | 01100101
f | 102 | 01100110
g | 103 | 01100111
h | 104 | 01101000
i | 105 | 01101001
j | 106 | 01101010
k | 107 | 01101011
l | 108 | 01101100
m | 109 | 01101101
n | 110 | 01101110
o | 111 | 01101111
p | 112 | 01110000

## Slide 15: Casting between Numeric Types
Casting from shorter to longer types preserves the value
Casting from longer to shorter types drops the high-order bits
Casting between signed/unsigned types preserves the bits (it just changes the interpretation)
Implicit casting occurs in assignments and parameter lists. In mixed expressions, signed values are implicitly cast to unsigned
    Source of many errors!
Notes: Note: casting part of signed demo

## Slide 16: Exercise 3: Casting
Assume you have a machine with 6-bit integers/3-bit shorts
Assume variables: int x = -17; short sy = -3;
Complete the following table
Expression | Decimal | Binary
x | -17 | 
sy | -3 | 
(unsigned int) x |  | 
(int) sy |  | 
(short) x |  | 

## Slide 17: When to Use Unsigned
Rarely
When doing multi-precision arithmetic, or when you need an extra bit of range … but be careful!
for (unsigned int i = cnt-2; i >= 0; i--){
a[i] += a[i+1];
}

## Slide 18: Hexadecimal Numbers
00101100 00110101 00110000 11100001
Dec | Hex
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
2
c
3
5
3
0
e
1
0x2c3530e1

## Slide 19: Exercise 3: Hexadecimal Numbers
Consider the following hexadecimal values. What is the representation of each value in binary?
  0x0a
  0x11
  0x2f
00001010 (10)
00010001 (17)
00101111 (47)

## Slide 20: Endianness
47 vs 74

## Slide 21: Endianness
Big Endian: low-order bits go on the right (40 + 7)
  Networks generally use big endian (aka network byte order)
Little Endian: low-order bits go on the left (7 + 40)
  Most modern machines use this representation
I will try to always be clear about whether I'm using a big endian or little endian representation
When in doubt, ask!

## Slide 22: Arithmetic Logic Unit (ALU)
circuit that performs bitwise operations and arithmetic on integer binary types

## Slide 23: Bitwise vs Logical Operations (in C)
Bitwise Operators &, |, ~, ^
  View arguments as bit vectors
  operations applied bit-wise in parallel
Logical Operators &&, ||, !
  View 0 as “False”
  View anything nonzero as “True”
  Always return 0 or 1
  Early termination
Shift operators <<, >>
  Left shift fills with zeros
  For unsigned integers, right shift is logical (fills with zeros)
  For signed integers, right shift is arithmetic (fills with high-order bit)

## Slide 24: Exercise 4: Bitwise vs Logical Operations
What is the binary representation of each of the following expressions? Assume signed char data type (one byte).
  ~(-30)
  -30 & 22
  -30 && 22
  22 << 1
  22 >> 1
  -30 >> 1
= ~(11100010) = 00011101 = 29
= 11100010 && 00010110 = 00000001 = 1
= 00010110 << 1 = 00101100 = 44
= 11100010 >> 1 = 11110001 = -15
= 11100010 & 00010110 = 00000010 = 2
= 00010110 >> 1 = 00001011 = 11

## Slide 25: Multiplying with Shifts
Multiplication is slow
Bit shifting is kind of like multiplication/division, and is often faster
  x * 8 = x << 3
  x * 10 = x << 3 + x << 1
Most compilers will automatically replace multiplications with shifts where possible
Notes: Hint about rounding errors with division

## Slide 26: Arithmetic Operations (in C)
Basic Math Operators +, -, *, /
  division is integer division (rounds towards zero)
Modulus Operator %
Increment/Decrement operators ++, --
  x++ is the same as x = x+1 or x += 1
  x-- is the same as x = x-1 or x -= 1

## Slide 27: Addition Example
Compute 5 + -3 assuming all ints are stored as four-bit signed values
0 1 0 1
+ 1 1 0 1
0
1
0
0
1
= 2 (Base-10)
1
Like you learned in grade school, only binary!
… and with a finite number of digits

## Slide 28: Addition/Subtraction with Overflow
Compute 5 + 6 assuming all ints are stored as four-bit signed values
0 1 0 1
+ 0 1 1 0
1
1
0
1
1
= -5 (Base-10)

## Slide 29: Error Cases
[ ]
representable values
[ ]

## Slide 30: Exercise 5: Binary Addition
Given the following 5-bit signed values, compute their sum and indicate whether or not an overflow occurred
x | y | x+y | overflow?
00010 | 00101 |  | 
01100 | 00100 |  | 
10100 | 10001 |  | 
00101
10000
00101
no
yes
yes
x+y | overflow?

## Slide 31: Multiplication Example
+ _
Compute 3 x 2 assuming all ints are stored as four-bit signed values
0 0 1 1
x 0 0 1 0
= 6 (Base-10)
0 0 0 0
0 0 1 1 0
0 1 1 0
Like you learned in grade school, only binary!
… and with a finite number of digits

## Slide 32: Multiplication Example
Compute 5 x 2 assuming all ints are stored as four-bit signed values
0 1 0 1
x 0 0 1 0
= -6 (Base-10)
0 0 0 0
0 1 0 1 0
+ _
1 0 1 0

## Slide 33: Error Cases
[ ]
representable values
[ )

## Slide 34: Exercise 6: Binary Multiplication
Given the following 3-bit signed values, compute their product and indicate whether or not an overflow occurred
x | y | x*y | overflow?
100 | 101 |  | 
010 | 011 |  | 
111 | 010 |  | 
100
110
110
yes
yes
no
x*y | overflow?