## Slide 1: Lecture 5: Arrays, Operations and Jumps in Assembly
CS 105 Spring 2026

## Slide 2: Logistical Note
Check In 1 in lab next week (Feb 18 or 19)
90 minutes
3 questions
1 page of written notes

## Slide 3: Review: Assembly/Machine Code View
Memory
0x7FFF
0x0000
Central Processing Unit (CPU)
Programmer-Visible State
  PC: Program counter (%rip)
  Register file: 16 Registers
  Float registers
  Condition codes
    Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
PC
Addresses
Instructions
Code
Data
Stack
Heap
Registers
Condition
Codes
Float registers

## Slide 4: Review: X86-64 Integer Registers
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
(second argument)
(first argument)
(stack pointer)
(third argument)
(fourth argument)
(function result)
(fifth argument)
(sixth argument)

## Slide 5: Review: Assembly Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Conditional branches
  Unconditional jumps to/from procedures

## Slide 6: Review: Operand Forms
Immediate:
  Syntax: $c Ex: $47 Val: c C Equiv: 47
Register:
  Syntax: r Ex: %rbp Val: Reg[r] C Equiv: x
Memory (Absolute):
  Syntax: addr Ex: 0x4050 Val: Mem[addr] C Equiv: *0x60201a
Memory (Indirect):
  Syntax: (r) Ex: (%rsp) Val: Mem[Reg[r]] C Equiv: *x
Notes: Note: done on board

## Slide 7: Review: Data Movement Instructions
MOV source, dest Move data source->dest
  movb Move 1 byte
  movw Move 2 bytes
  movl Move 4 bytes
  movq Move 8 bytes

## Slide 8: Example 1: Array Accessing
Register %rdi contains starting address of array zipcode
Desired digit at %rdi
Use indirect memory reference (%rdi) or raw address for absolute memory reference 0x14
int get_first_digit(int* zipcode){
return zipcode[0];
}
movl (%rdi), %eax # ret = z[0]
zip_code pomona;
9
1
7
1
1
16
20
24
28
32
36
Register | Use(s)
%rdi | zipcode
%rax | return val

## Slide 9: Example 2: Array Accessing
int get_digit(int* zipcode, int digit){
return zipcode[digit];
}
???
zip_code pomona;
9
1
7
1
1
16
20
24
28
32
36
Register | Use(s)
%rdi | zipcode
%rsi | digit
%rax | return val

## Slide 10: Operand Forms
Immediate:
  Syntax: $c Ex: $47 Val: c C Equiv: 47
Register:
  Syntax: r Ex: %rbp Val: Reg[r] C Equiv: x
Memory (Absolute):
  Syntax: addr Ex: 0x4050 Val: Mem[addr] C Equiv: *0x60201a
Memory (Indirect):
  Syntax: (r) Ex: (%rsp) Val: Mem[Reg[r]] C Equiv: *x
Memory (Base+displacement):
  Syntax: c(r) Ex: 12(%rsp) Val: Mem[Reg[r]+c] C Equiv: *(x+12)
Memory (Scaled indexed):
  Syntax: (r1,r2,s) Ex: (%rdx,%rsi,4) Val: Mem[Reg[r1]+Reg[r2]*s] C: r1[r2]
Memory (Scaled indexed w/ displacement):
  Syntax: c(r1,r2,s) Ex: 8(%rdx,%rsi,4) Val: Mem[Reg[r1]+Reg[r2]*s+c] C: (r1+8)[r2]
Notes: Note: done on board

## Slide 11: Example 2: Array Accessing
Register %rdi contains starting address of array zipcode
Register %rsi contains array index digit
Desired digit at %rdi + 4*%rsi
Use memory reference (%rdi,%rsi,4)
int get_digit(int* zipcode, int digit){
return z[digit];
}
movl (%rdi,%rsi,4), %eax # ret = z[digit]
zip_code pomona;
9
1
7
1
1
16
20
24
28
32
36
Register | Use(s)
%rdi | z
%rsi | digit
%rax | return val

## Slide 12: Structure Representation
Structure represented as block of memory
  Big enough to hold all of the fields
Fields ordered according to declaration
  Even if another ordering could yield a more compact representation
Compiler determines overall size + positions of fields
  Machine-level program has no understanding of the structures in the source code
z
r
next
0
20
24
32
typedef struct node {
int z[5];
struct node* next;
} node_t;

## Slide 13: Accessing Fields
# n in %rdi
movq 24(%rdi), %rax
ret
node_t* get_next(node_t* n){
return n->next;
}
Accessing a field in a struct
  Offset of each structure member determined at compile time
r + 24
z
r
next
0
20
24
32
typedef struct node {
int z[5];
struct node* next;
} node_t;
Register | Use(s)
%rdi | n
%rax | return val

## Slide 14: Exercise 1: Operands
What are the values of the following operands (assuming register and memory state shown above)?
  (%rax,%rcx,4)
  (%rax,%rdx,2)
  1(%rax,%rcx,4)
Register | Value
%rax | 0x108
%rcx | 0x01
%rdx | 0x03
0xAB
0x07
0x2F
Memory Address | Value
0x108 | 0xFF
0x109 | 0x47
0x10a | 0x13
0x10b | 0xE1
0x10c | 0xAB
0x10d | 0x2F
0x10e | 0x07

## Slide 15: Arithmetic in Assembly

## Slide 16: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
    xorq Src,Dest Dest = Dest ^ Src
    shlq Src,Dest Dest = Dest << Src Also called salq
    shrq Src,Dest Dest = Dest >> Src Logical
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
char | b | 1
short | w | 2
int | l | 4
long | q | 8
pointer | q | 8
Suffixes
Notes: different signed and unsigned multiply b/c need to set condition bits differently (e.g., overflow for -1*-1 vs 0xFFFF*0xFFFF

## Slide 17: Some Arithmetic Operations
One Operand Instructions
    notq Dest Dest = ~Dest
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
char | b | 1
short | w | 2
int | l | 4
long | q | 8
pointer | q | 8
Suffixes

## Slide 18: Exercise 2: Assembly Operations
Value | Location
addq $0x47, %rax
subq %rax, %rbx
addq (%rbx), %rax
shlq %rdi, (%rax)
addq (%rax,%rdi,8), %rax
Register | Value
%rax | 0x100
%rbx | 0x110
%rdi | 0x02
Address | Value
0x100 | 0x012
0x108 | 0x99a
0x110 | 0x809
0x147
0x010
0x909
0x048
0x909
%rax
%rbx
%rax
Mem[0x100]
%rax
Value | Location

## Slide 19: Example: Translating Assembly
arith:
orq %rsi, %rdi
sarq $3, %rdi
notq %rdi
movq %rdx, %rax
subq %rdi, %rax
ret
Interesting Instructions
  sarq: arithmetic right shift
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | return value
long arith(long x, long y, long z){
x = x | y;
x = x >> 3;
x = ~x;
long ret = z - x;
return ret;
}

## Slide 20: lea Instruction
Scaled Memory Operands
movq (%rdi,%rsi,8), %rax
leaq Source, Dest
leaq (%rdi,%rsi,8), %rax
pointer arithmetic
  E.g., p = x + i;
arithmetic
  expressions x + k*y (k=1, 2, 4, 8)
void ex1(long* xp, long yp){
long* p = xp + yp;
long ret = *p;
}
void ex2(long* xp, long yp){
long* ret = xp + yp;
}
void ex3(long xp, long yp){
long ret = xp + 8*yp;
}
long m12(long x){
return x*12;
}
leaq (%rdi,%rdi,2), %rax # ret <- x+x*2
salq $2, %rax # return ret<<2
Used by compiler to optimize:

## Slide 21: Conditional Jumps

## Slide 22: Jumps
A jump instruction can cause the execution to switch to a completely new position in the program (updates the program counter)
  jmp Label
  jmp *Operand
.L0:
movq $0, %rax
jmp .L1
movq (%rax), %rdx
.L1:
movq %rcx, %rax
jmp *%rdi

## Slide 23: Conditional Jumps
jX instructions
  Jump to different part of code if condition is true
jX | Description
jmp | Unconditional
je | Equal to Zero
jne | Not Equal to Zero
js | Negative
jns | Nonnegative
jl | Less (Signed)
jle | Less or Equal (Signed)
jg | Greater (Signed)
jge | Greater or Equal (Signed)
What condition are we evaluating?
Notes: js SF Negative
jns ~SF Nonnegative

## Slide 24: Conditional Jumps
Whether or not we jump depends on how the output of the last arithmetic operation compares to zero
Not set by lea instruction
Unless there's an explicit conditional evaluation more recently
movq $47, %rax
subq $13, %rax
jg .L2
movq $47, %rax
subq $13, %rax
je .L2
jump
no jump

## Slide 25: Condition Evaluations
cmp a,b like computing b-a without setting destination
test a,b like computing a&b without setting destination

## Slide 26: Exercise 2: Conditional Jumps
Consider each of the following segments of assembly code, and indicate whether or not the jump will occur. In all cases, assume that %rdi contains the value 47 and %rsi contains the value 13
  addq %rdi, %rsi
  je .L0
  subq %rdi, %rsi
  jge .L0
  cmpq %rdi, %rsi
  jl .L0
  testq %rdi, %rdi
  jne .L0
no jump
no jump
jump
jump

## Slide 27: Branches and Jumps
Processor state (partial)
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of next instruction to execute ( %rip )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Program counter
CF
ZF
SF
OF
Condition codes
%rsp (stack ptr)
%r8 (5th arg)
%r9 (6th arg)
%r10
%r11
%r12
%r13
%r14
%r15
%rax (return val)
%rbx
%rcx (4th arg)
%rdx (3rd arg)
%rsi (2nd arg)
%rdi (1st arg)
%rbp

## Slide 28: Condition Codes
Single bit registers
    ZF Zero Flag
    PF Parity Flag
    SF Sign Flag (for signed)
    OF Overflow Flag (for signed)
    CF Carry Flag (for unsigned)
Implicitly set (as a side effect) by arithmetic operations
Explicitly set by cmp and test
Not set by leaq instruction

## Slide 29: Example Condition Codes: compare
Instruction cmp explicitly sets condition codes
cmpq a,b like computing b-a without setting destination
  ZF set if (b-a) == 0
  PF set if (b-a)% 2 == 1
  SF set if (b-a) < 0 (as signed)
  OF set if two’s-complement (signed) overflow
  CF set if carry out from most significant bit (used for unsigned comparisons)

## Slide 30: Jumping
jX instructions
  Jump to different part of code if condition is true
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jl | (SF^OF) | Less (Signed)
jle | (SF^OF) ¦ ZF | Less or Equal (Signed)
jg | ~(SF^OF) & ~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jb | CF | Below (unsigned)
jbe | CF ¦ ZF | Below or Equal (Signed)
ja | ~ZF & ~CF | Above (unsigned)
jae | ~CF | Above or Equal (Signed)
Notes: js SF Negative
jns ~SF Nonnegative

## Slide 31: Reading Condition Codes
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF ^ OF) & ~ZF | Greater (signed)
setge | ~(SF ^ OF) | Greater or Equal (signed)
setl | SF ^ OF | Less (signed)
setle | (SF ^ OF) ¦ ZF | Less or Equal (signed)

## Slide 32: Reading Condition Codes
setX instruction: set a single byte based on condition codes
Does not alter remaining bytes of destination
Typically use movz to set the rest of the bits to zero
long gt (long x, long y){
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
gt:
cmpq %rsi, %rdi # set flags for x-y
setg %al # ~(SF^OF)&~ZF, True when x > y
movzbq %al, %rax # Zero rest of %rax
ret # return