## Slide 1: Lecture 10: Caches
CS 105 Spring 2026

## Slide 2: Review: Machine Code View
Memory
0x7FFF
0x0000
Central Processing Unit (CPU)
Programmer-Visible State
  PC: Program counter (%rip)
  Register file: 16 Registers
  Float registers
  Condition codes
    Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
PC
Addresses
Instructions
Code
Data
Stack
Heap
Registers
Condition
Codes
Float registers
ALU

## Slide 3: A Computer System
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Expansion slots for
other devices such
as network adapters
hello executable
stored on disk
PC

## Slide 4: The CPU-Memory Gap
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
Notes: two numbers for CPU: actual cycle time (white squares) and effective CPU cycle time (allows for parallelization, circles)

## Slide 5: Life without caches
You decide that you want to learn more about computer systems than is covered in this course
The library contains all the books you could possibly want, but you don't like to study in libraries, you prefer to study in your dorm room.
You have the following constraints:
Desk
(can hold one book)
Library
(can hold many books)

## Slide 6: Quantifying Speed (without caches)
Average latency to access a book: 40mins
Average throughput (incl. reading time): 1.2 books/hr
Need book 1
Checkout book 1 (10 mins)
Read book 1 (10 mins)
Need book 2
Return book 1
Checkout book 2 (10 mins)
Return book 2
Checkout book 1 (10 mins)
Read book 2 (10 mins)
Need book 1 again!
Read book 1 (10 mins)
Walk to library (15mins)
Walk to library (15mins)
Walk to library (15mins)
Walk to dorm (15mins)
Walk to dorm (15mins)
Walk to dorm (15mins)
Notes: latency: each time takes 40 mins to access book (15*2 walking + 10mins checkout) throughput: read 3 books in 2.5 hours -> 3/2.5 = 1.2 books/hour

## Slide 7: The CPU-Memory Gap
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SRAM
Notes:   SRAM: Faster (only 10 or so times slower than the CPU)
  Expensive (1000x relative to DRAM)

## Slide 8: Latency numbers (2020)
Register access | 0.3 ns | 
L1 cache reference | 1 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 3,000 ns | 3 s
Register access | 0.3 ns | 
L1 cache reference | 1 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 3,000 ns | 
SSD random read | 16,000 ns | 16 s
SSD 1MB sequential read | 49,000 ns | 49 s
Magnetic Disk seek | 2,000,000 ns | 2 ms
Magnetic Disk 1MB sequential read | 825,000 ns | 825 s
SSD random read | 16,000 ns | 
SSD 1MB sequential read | 49,000 ns | 
Magnetic Disk seek | 2,000,000 ns | 2 ms
Magnetic Disk 1MB sequential read | 825,000 ns | 
Round trip in Datacenter | 500,000 ns | 500 s
Round trip CA<->Europe | 150,000,000 ns | 150 ms
Round trip in Datacenter | 500,000 ns | 
Round trip CA<->Europe | 150,000,000 ns | 150 ms
Notes: https://people.eecs.berkeley.edu/~rcs/research/interactive_latency.html
register access ~.2-.4ns (2.6 GHz cycle => register ~.38ns )

## Slide 9: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 10: Life with caching
Average latency to access a book: <20mins
Average throughput (incl. reading time): ~2 books/hr
Need book 1
Checkout book 1 & 2 (10 mins)
Read book 1 (10 mins)
Need book 2
Read book 2 (10 mins)
Need book 1 again!
Walk to library (15mins)
Check bookshelf (5mins)
Walk to dorm (15mins)
Find book 2!
Check bookshelf (5mins)
Find book 1!
Check bookshelf (5mins)
Read book 1 (10 mins)
Notes: average latency: (45 + 5 + 5)/3 = 18.3 minutes
throughput: read 3 books in 85 minutes = 2.1 books/hr

## Slide 11: Caching—The Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)

## Slide 12: Exercise 1: Caching Strategies
I want to refresh on Return-Oriented Programming. In the library, there is a book about:
C-programming,
Assembly Instructions,
Assembly Function Calls,
Register Usage,
Buffer Overflows,
and Return-Oriented Programming.
My bookshelf can hold three books at a time. How should we decide which books to keep in the bookshelf?

## Slide 13: Example Access Patterns
Data references
  Reference array elements in succession.
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
int sum = 0;
for (int i = 0; i < n; i++){
sum += a[i];
}
return sum;

## Slide 14: Principle of Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 15: Cache Organization

## Slide 16: Cache Lines
data block: cached data (i.e., copy of bytes from memory)
tag: uniquely identifies which data is stored in the cache line
valid bit: indicates whether or not the line contains meaningful information
0
1
2
7
tag
v
3
6
5
4
valid bit
tag
data block

## Slide 17: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
0
1
2
n-1
find line
identifies byte in line
Notes: Note: low-order bits are always zero if we assume 4-byte words (since we'll always be looking up the address of a word), but we'll just think about those bits as part of the offset

## Slide 18: Example: Direct-mapped Cache
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Assume: cache block size 8 bytes, total cache size 32 bytes
Address of data:
Assume: assume 8-bit machine
0xB4
1011 0100
3 bit tag
2 bit index
3 bit offset
101
100
10
Line 0
Line 1
Line 2
Line 3

## Slide 19: Exercise 2: Interpreting Addresses
Consider the 12-bit address 0xA59. What would be the tag, index, and offset for this address with each of the following cache configurations?
A direct-mapped cache with 8 cache lines and 8-byte data blocks
A direct-mapped cache with 16 cache lines and 4-byte data blocks
A direct-mapped cache with 16 cache lines and 8-byte data blocks
tag = 1010 01 = 0x29
0xA59 = 1010 0101 1001
index = 011 = 0x3
offset = 001 = 0x1
tag = 1010 01 = 0x29
index = 0110 = 0x6
offset = 01 = 0x1
tag = 1010 0 = 0x14
index = 1011 = 0xB
offset = 001 = 0x1
Notes: 1. 6 tag, 3 index, 3 offset 2. 6 tag, 4 index, 2 offset 2. 5 tag, 4 index, 3 offset

## Slide 20: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
0
1
2
n-1
Checking the cache (i.e., "bookshelf"):
index tells you which line to check
Is that line valid?
  If no, cache miss
Does the tag match?
  If no, cache miss
If valid and tag matches, cache hit!
  Read from datablock at offset
check value
valid?
Notes: Note: low-order bits are always zero if we assume 4-byte words (since we'll always be looking up the address of a word), but we'll just think about those bits as part of the offset

## Slide 21: Exercise 3: Cache Hits and Misses
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Assume: cache block size 8 bytes, total cache size 32 bytes
Assume: assume 8-bit machine
Line 0
Line 1
Line 2
Line 3
For each address, is it a hit or
a miss? For hits, what data is at that address in memory?
0x2D
0x2E
0x74
0x3A
001
101
01
Hit 0x40
001
110
01
Hit 0x06
011
100
10
Miss
001
010
11
Miss

## Slide 22: Handling a Cache Miss
When a cache miss occurs update cache line at that index:
  Replace data block with bytes from memory
    Copies all bytes with same tag + index
  Update tag
  Set valid bit to 1 (if not already)
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Line 0
Line 1
Line 2
Line 3
Address of data:
0x74
0111 0100
3 bit tag
2 bit index
3 bit offset
011
100
10
0x73
0x72
0x71
0x70
0x6F
0x6E
47
00
33
2F
0A
1A
0x79
0x78
0x77
0x76
0x75
0x74
B7
AB
64
15
E0
23
011
1
2F
33
47
64
1A
15
E0
AB

## Slide 23: Exercise 4: Direct-mapped Cache
Line 0 |  |  | Line 1 |  | 
0 |  | 47 48 | 0 |  | 49 50
Cache
Assume 8 byte data blocks
18
Memory
0x74
0x70
0x6c
0x68
0x64
0x60
17
13
16
15
14
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x70 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
How well does this take advantage of spatial locality?
How well does this take advantage of temporal locality?
000
0
0110
Miss
1
0110
13 14
100
0
0110
Hit
000
0
0111
Miss
1
0111
17 18
100
0
0110
Miss
100
0
0110
Hit
1
0110
13 14
000
0
0110
Hit
13
14
17
14
14
13
1
0110
13 14
1
0110
13 14
1
0110
13 14
0
0000
49 50
0
0000
49 50
0
0000
49 50
0
0000
49 50
0
0000
49 50
0
0000
49 50
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x70 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
Line 0 |  |  | Line 1 |  | 
0 |  | 47 48 | 0 |  | 49 50
0000
0000
Time
Notes: Same setup, except now assume 8 byte data blocks, 2 cache lines