## Slide 1: Lecture 11: Caches (cont'd)
CS 105 Spring 2026

## Slide 2: Review: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
0
1
2
n-1
Checking the cache (i.e., "bookshelf"):
index tells you which line to check
Is that line valid?
  If no, cache miss
Does the tag match?
  If no, cache miss
If valid and tag matches, cache hit!
  Read from datablock at offset
valid bit
tag
data block
Notes: Note: low-order bits are always zero if we assume 4-byte words (since we'll always be looking up the address of a word), but we'll just think about those bits as part of the offset

## Slide 3: Handling Cache Miss
When a cache miss occurs update cache line at that index:
  Replace data block with bytes from memory
    Copies all bytes with same tag + index
  Update tag
  Set valid bit to 1 (if not already)
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Line 0
Line 1
Line 2
Line 3
Address of data:
0x74
0111 0100
3 bit tag
2 bit index
3 bit offset
011
100
10
0x73
0x72
0x71
0x70
0x6F
0x6E
47
00
33
2F
0A
1A
0x79
0x78
0x77
0x76
0x75
0x74
B7
AB
64
15
E0
23
011
1
2F
33
47
64
1A
15
E0
AB

## Slide 4: Direct-mapped Cache Example
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  | 
0 | 0 | 47 48 | 0 | 8 | 49 50 | 0 | a | 51 52 | 0 | 1 | 53 54
Cache
Assume 8 byte data blocks (fit 2 ints)
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
How well does this take advantage of spatial locality?
How well does this take advantage of temporal locality?
000
00
011=0x3
Miss
100
00
011=0x3
Hit
000
00
100=0x4
Miss
100
00
011=0x3
Miss
100
00
011=0x3
Hit
000
00
011=0x3
Hit
13
14
21
14
14
13
Time
1
3
13 14
0
8
49 50
0
a
51 52
0
1
53 54
1
4
21 22
0
8
49 50
0
a
51 52
0
1
53 54
1
3
13 14
0
8
49 50
0
a
51 52
0
1
53 54
1
3
13 14
0
8
49 50
0
a
51 52
0
1
53 54
1
3
13 14
0
8
49 50
0
a
51 52
0
1
53 54
1
3
13 14
0
8
49 50
0
a
51 52
0
1
53 54
000
00
100=0x4
Miss
21
1
4
21 22
0
8
49 50
0
a
51 52
0
1
53 54
18
17
20
19
14
13
16
15
22
21
0x60
0x64
0x68
0x6c
0x70
0x74
0x78
0x7c
0x80
0x84
Memory
Notes: Same setup, except now assume 8 byte data blocks, 2 cache lines

## Slide 5: 2-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Address of data:
tag
offset
index
the rest of the bits
log(# sets) bits
log(block size) bits
Set 0
Set 1
Set 2
Set n-1

## Slide 6: Exercise: 2-way Set Associative Cache
rd 0x70 |  |  |  |  | 
Cache
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
000
0
0110=0x6
Miss
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
Set 0 | Set 1
Set 0
Set 1
100
0
0110=0x6
Hit
000
0
1000=0x8
Miss
100
0
0110=0x6
Hit
100
0
0110=0x6
Hit
000
0
0110=0x6
Hit
000
0
1000=0x8
Hit
000
0
0111=0x7
Miss
18
17
20
19
14
13
16
15
22
21
0x60
0x64
0x68
0x6c
0x70
0x74
0x78
0x7c
0x80
0x84
Memory
6
1
13 14
1
0
47 48
0
0
47 48
1
0
47 48
6
1
13 14
1
0
47 48
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
13
14
21
14
14
13
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
21
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
Time
Assume 8 byte data blocks (fit 2 ints)
Notes: Same setup, except now assume 8 byte data blocks, 2 cache lines

## Slide 7: Eviction from the Cache
On a cache miss, a new block is loaded into the cache
Direct-mapped cache: A valid block at the same location must be evicted—no choice
Associative cache: If all blocks in the set are valid, one must be evicted
  Random policy
  FIFO
  LIFO
  Least-recently used; requires extra data in each set
  Most-recently used; requires extra data in each set
  Most-frequently used; requires extra data in each set
  Least-recently used; requires extra data in each set

## Slide 8: Exercise: 2-way Set Associative Cache
rd 0x70 |  |  |  |  | 
Cache
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
000
0
0110=0x6
Miss
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
Set 0 | Set 1
Set 0
Set 1
100
0
0110=0x6
Hit
000
0
1000=0x8
Miss
100
0
0110=0x6
Hit
100
0
0110=0x6
Hit
000
0
0110=0x6
Hit
000
0
1000=0x8
Hit
000
0
0111=0x7
Miss
18
17
20
19
14
13
16
15
22
21
0x60
0x64
0x68
0x6c
0x70
0x74
0x78
0x7c
0x80
0x84
Memory
6
1
13 14
1
0
47 48
0
0
47 48
1
0
47 48
6
1
13 14
1
0
47 48
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
6
1
13 14
8
1
21 22
0
0
47 48
1
0
47 48
13
14
21
14
14
13
21
Access | tag | idx | off | h/m | val
rd 0x60 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x60 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
rd 0x70 |  |  |  |  | 
7
1
17 18
8
1
21 22
0
0
47 48
1
0
47 48
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
Time
Assume 8 byte data blocks (fit 2 ints)
Notes: Same setup, except now assume 8 byte data blocks, 2 cache lines

## Slide 9: Caching and Writes
What to do on a write-hit?
  Write-through: write immediately to memory
  Write-back: defer write to memory until replacement of line
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate: load into cache, update line in cache
    Good if more writes to the location follow
  No-write-allocate: writes straight to memory, does not load into cache
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 10: Exercise: Write-through + No-write-allocate
Cache
Memory
0x24
0x20
0x1c
0x18
0x14
0x10
21
17
20
19
18
22
Assume 4 byte data blocks
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 
0001
00
00
m
1
1
17
0001
00
00
h
1
1
8
0010
01
00
m
2
1
9
0010
01
00
m
0010
00
00
m
2
1
21
N
Y
Y
N
N
8
9
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 

## Slide 11: Exercise: Write-back + Write-allocate
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 48 | 0 | 8 | 49 50 | 0 | a | 51 52 | 0 | 1 | 53 54 | 
Access | tag | idx | off | h/m | Val
rd 0x74 |  |  |  |  | 
wr 8,0x70 |  |  |  |  | 
wr 9,0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
011
10
100
m
011
10
000
h
011
00
100
m
011
00
100
h
100
00
000
m
N
N
N
N
Y
Cache
18
17
20
19
14
13
16
15
22
21
0x60
0x64
0x68
0x6c
0x70
0x74
0x78
0x7c
0x80
0x84
Memory
0
0
47 48
0
8
49 50
1
3
17 18
0
1
53 54
1
3
13 9
0
8
49 50
1
3
8 18
0
1
53 54
1
3
13 9
0
8
49 50
1
3
8 18
0
1
53 54
1
4
21 22
0
8
49 50
1
3
8 18
0
1
53 54
0
0
47 48
0
8
49 50
1
3
8 18
0
1
53 54
9
13
D
D
D
D
D
D
18
9
21
18
17
20
19
14
13
16
15
22
21
0x60
0x64
0x68
0x6c
0x70
0x74
0x78
0x7c
0x80
0x84
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 48 | 0 | 8 | 49 50 | 0 | a | 51 52 | 0 | 1 | 53 54 | 
Access | tag | idx | off | h/m | Val
rd 0x74 |  |  |  |  | 
wr 8,0x70 |  |  |  |  | 
wr 9,0x64 |  |  |  |  | 
rd 0x64 |  |  |  |  | 
rd 0x80 |  |  |  |  | 
Assume 8 byte data blocks (fit 2 ints)

## Slide 12: Caching Organization Summarized
A cache consists of lines
A line contains
  A block of bytes, the data values from memory
  A tag, indicating where in memory the values are from
  A valid bit, indicating if the data are valid
Lines are organized into sets
  Direct-mapped cache: one line per set
  k-way associative cache: k lines per set
  Fully associative cache: all lines in one set
Caches handle both reads and writes
  write-through: write to both cache and memory
  write-back: write only to cache, write to memory on evict,
  write-allocate: alloc on any miss
  no-write allocate: alloc only on read miss

## Slide 13: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 14: Typical Intel Core i7 Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 d-cache and i-cache:
  32 KB, 8-way
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way
  Access: 40-75 cycles
Block size: 64 bytes for all caches.
Notes: all use varients/approximations of LRU for eviction
All three levels of cache are write back. L1 is write no-allocate, L2 and L3 are write allocate.
https://www.edn.com/memory-hierarchy-design-part-6-the-intel-core-i7-fallacies-and-pitfalls/

## Slide 15: Caching Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)
Miss rate: the fraction of accesses that are misses
Hit time: the time to process a hit
Miss penalty: the additional time to process a miss
Average access time: hit-time + miss-rate * miss-penalty

## Slide 16: Categorizing Misses
Compulsory: first-reference to a block
Capacity: cache is too small to hold all of the data
Conflict: collisions in a specific set
Average access time: hit-time + miss-rate * miss-penalty
Notes: Larger block size will reduce compulsory misses
Larger associativity will reduce conflict misses
Larger cache will reduce capacity misses
But: larger block size yields larger miss penalty (more data to copy from memory)
larger cache (and larger associativity): increased hit time
Classifying misses with a particular cache configuration:
  Would this miss occur in a cache with infinite capacity? If the answer is yes, then this is a compulsory miss and we are done. If the answer is no, then consider question 2.
  Would this miss occur in a fully associative cache with the desired capacity? If the answer is yes, then this is a capacity miss and we are done. If the answer is no, then consider question 3.
  Would this miss occur in a cache with the desired capacity and associativity? If the answer is yes, then this is a conflict miss and we are done. If the answer is no, then this is not a miss – it is a hit!