## Slide 1: Lecture 10: Caches
CS 105 October 8, 2019

## Slide 2: Life without caches
You decide that you want to learn more about computer systems than is covered in this course
The library contains all the books you could possibly want, but you don't like to study in libraries, you prefer to study at home.
You have the following constraints:
Desk
(can hold one book)
Library
(can hold many books)

## Slide 3: Life without caches
Average latency to access a book: 40mins
Average throughput (incl. reading time): 1.2 books/hr

## Slide 4: A Computer System
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Expansion slots for
other devices such
as network adapters
hello executable
stored on disk
PC

## Slide 5: The CPU-Memory Gap
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk
SRAM
Notes:   SRAM: Faster (only 10 or so times slower than the CPU)
  Expensive (1000x relative to DRAM)

## Slide 6: Caching—The Very Idea
Keep some memory values nearby in fast memory
Modern systems have 3 or even 4 levels of caches
Cache idea is widely used:
  Disk controllers
  Web
  (Virtual memory: main memory is a “cache” for the disk)

## Slide 7: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 8: Latency numbers every programmer should know (2019)
L1 cache reference | 1 ns | 
Branch mispredict | 3 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 4,000 ns | 4 s
SSD random read | 16,000 ns | 16 s
SSD 1MB sequential read | 62,000 ns | 62 s
Disk random read | 3,000,000 ns | 3 ms
Disk 1MB sequential read | 947,000 ns | < 1 ms
Round trip in Datacenter | 500,000 ns | 500 s
Round trip CA<->Europe | 150,000,000 ns | 150 ms
L1 cache reference | 1 ns | 
Branch mispredict | 3 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 4,000 ns | 
SSD random read | 16,000 ns | 
SSD 1MB sequential read | 62,000 ns | 
Disk random read | 3,000,000 ns | 3 ms
Disk 1MB sequential read | 947,000 ns | < 1 ms
Round trip in Datacenter | 500,000 ns | 
Round trip CA<->Europe | 150,000,000 ns | 150 ms
Notes: https://people.eecs.berkeley.edu/~rcs/research/interactive_latency.html

## Slide 9: Life with caching
Average latency to access a book: <20mins
Average throughput (incl. reading time): ~2 books/hr

## Slide 10: Caching—The Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)
Miss rate: the fraction of accesses that are misses
Hit time: the time to process a hit
Miss penalty: the additional time to process a miss
Average access time: hit-time + miss-rate * miss-penalty

## Slide 11: Question: how do we decide which books to put on the bookshelf?

## Slide 12: Example Access Patterns

## Slide 13: Principle of Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 14: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 15: Locality Example
Which of the following functions is better in terms of locality with respect to array src?
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
81.8ms
4.3ms
2.0 GHz Intel Core i7 Haswell

## Slide 16: Another Locality Example
How would you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N]){
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[i][j][k];
return sum;
}

## Slide 17: Cache Organization

## Slide 18: Word-oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by m=4 (32-bit) or m=8 (64-bit)
There are (up to) unique addressable locations in memory
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
words
Bytes
Addr.
0003
0002
0001
0000
64-bit
words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0012
0008
0004
0000
0008
0000
Notes: I don't think words are really worth discussing

## Slide 19: Cache Lines
data block: cached data
tag: uniquely identifies which data is stored in the cache line
valid bit: indicates whether or not the line contains meaningful information
0
1
2
7
tag
v
3
6
5
4
valid bit
tag
data block

## Slide 20: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
Notes: Note: low-order bits are always zero if we assume 4-byte words (since we'll always be looking up the address of a word), but we'll just think about those bits as part of the offset

## Slide 21: Example: Direct-mapped Cache
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Assume: cache block size 8 bytes
Address of data:
Assume: assume 8-bit machine
0xB4
1011 0100
3 bit tag
2 bit index
3 bit offset
101
100
10
Line 0
Line 1
Line 2
Line 3

## Slide 22: Exercise: Direct-mapped Cache
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?
Transaction Stream
rd 0x00
rd 0x04
rd 0x10
rd 0x00
rd 0x04
rd 0x20
Memory
rd 0x14
rd 0x10
rd 0x0c
rd 0x08
rd 0x04
rd 0x00
17
13
16
15
14
Cache
Transaction | tag | index | h/m | Line 0 | Line 1
rd 0x00 |  |  |  | ? | ?
rd 0x04 |  |  |  |  | 
rd 0x10 |  |  |  |  | 
rd 0x00 |  |  |  |  | 
rd 0x04 |  |  |  |  | 
rd 0x10 |  |  |  |  | 
18
Line 2 | Line 3
? | ?
Assume 4 byte data blocks
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 23: Exercise: Direct-mapped Cache
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?
Transaction Stream
rd 0x00
rd 0x04
rd 0x10
rd 0x00
rd 0x04
rd 0x20
Memory
rd 0x14
rd 0x10
rd 0x0c
rd 0x08
rd 0x04
rd 0x00
17
13
16
15
14
Cache
Transaction | tag | index | h/m | Line 0 | Line 1
rd 0x00 |  |  |  | ? | ?
rd 0x04 |  |  |  |  | 
rd 0x10 |  |  |  |  | 
rd 0x00 |  |  |  |  | 
rd 0x04 |  |  |  |  | 
rd 0x10 |  |  |  |  | 
18
Assume 8 byte data blocks
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines