## Slide 1: Lecture 11: Caches (cont'd)
CS 105 October 10, 2019

## Slide 2: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 3: Principle of Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 4: Cache Lines
data block: cached data
tag: uniquely identifies which data is stored in the cache line
valid bit: indicates whether or not the line contains meaningful information
0
1
2
7
tag
v
3
6
5
4
valid bit
tag
data block

## Slide 5: Caching—The Organization
An address is decomposed into three parts
  Low-order b bits, providing an offset into a block (2b is the data block size)
  Middle s bits, indicating which set in the cache to search (2s is the number of sets)
  Upper remaining bits, the tag to be matched
Address of data:
tag
offset
index

## Slide 6: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?

## Slide 7: 2-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Address of data:
tag
offset
index
the rest of the bits
log(# sets) bits
log(block size) bits

## Slide 8: Exercise: 2-way Set Associative Cache
Cache
Transaction | tag | index | h/m
rd 0x00 |  |  | 
rd 0x04 |  |  | 
rd 0x14 |  |  | 
rd 0x00 |  |  | 
rd 0x04 |  |  | 
rd 0x10 |  |  | 
rd 0x20 |  |  | 
Memory
rd 0x14
rd 0x10
rd 0x0c
rd 0x08
rd 0x04
rd 0x00
17
13
16
15
14
18
Line 0 | Line 1 | Line 0 | Line 1
? | ? | ? | ?
Assume 8 byte data blocks
Set 0
Set 1
Set 0 | Set 1
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 9: Eviction from the Cache
On a cache miss, a new block is loaded into the cache
Direct-mapped cache: A valid block at the same location must be evicted—no choice
Associative cache: If all blocks in the set are valid, one must be evicted
  Random policy
  FIFO
  LIFO
  Least-recently used; requires extra data in each set
  Most-recently used; requires extra data in each set

## Slide 10: Caching Organization Summarized
A cache consists of lines
A line contains
  A block of bytes, the data values from memory
  A tag, indicating where in memory the values are from
  A valid bit, indicating if the data are valid
Lines are organized into sets
  Direct-mapped cache: one line per set
  k-way associative cache: k lines per set
  Fully associative cache: all lines in one set

## Slide 11: Caching and Writes
What to do on a write-hit?
  Write-through: write immediately to memory
  Write-back: defer write to memory until replacement of line
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate: load into cache, update line in cache
    Good if more writes to the location follow
  No-write-allocate: writes straight to memory, does not load into cache
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 12: Example: Write-through + No-write-allocate
Line 0 | Line 1 | Line 2 | Line 3 | W
? | ? | ? | ? | ?
Transaction | tag | index | h/m
rd 0x10 |  |  | 
wr 0x10 |  |  | 
wr 0x24 |  |  | 
rd 0x24 |  |  | 
rd 0x20 |  |  | 
Cache
Memory
rd 0x24
rd 0x20
rd 0x1c
rd 0x18
rd 0x14
rd 0x10
21
17
20
19
18
22
Assume 4 byte data blocks

## Slide 13: Exercise: Write-back + Write-allocate
Cache
Memory
rd 0x24
rd 0x20
rd 0x1c
rd 0x18
rd 0x14
rd 0x10
21
17
20
19
18
22
Assume 4 byte data blocks
Line 0 | Line 1 | Line 2 | Line 3 | W
? | ? | ? | ? | ?
Transaction | tag | index | h/m
rd 0x10 |  |  | 
wr 0x10 |  |  | 
wr 0x24 |  |  | 
rd 0x24 |  |  | 
rd 0x20 |  |  | 

## Slide 14: Categorizing Misses
Compulsory: first-reference to a block
Capacity: cache is too small to hold all of the data
Conflict: collisions in a specific set
Classifying misses in a cache with a target capacity and associativity as a sequence of three questions:
  Would this miss occur in a cache with infinite capacity? If the answer is yes, then this is a compulsory miss and we are done. If the answer is no, then consider question 2.
  Would this miss occur in a fully associative cache with the desired capacity? If the answer is yes, then this is a capacity miss and we are done. If the answer is no, then consider question 3.
  Would this miss occur in a cache with the desired capacity and associativity? If the answer is yes, then this is a conflict miss and we are done. If the answer is no, then this is not a miss – it is a hit!
Notes: Larger block size will reduce compulsory misses
Larger associativity will reduce conflict misses
Larger cache will reduce capacity misses
But: larger block size yields larger miss penalty (more data to copy from memory)
larger cache (and larger associativity): increased hit time

## Slide 15: Typical Intel Core i7 Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 16: Example: Cache-Aware Optimization
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 17: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik
jki / kji
kij / ikj

## Slide 18: Pentium III Xeon Matrix Multiply Performance
blocked matrix mutiply
jki / kji
kij / ikj
ijk / jik