## Slide 1: Lecture 7: Memory and the Stack
CS 51P September 25, 2019

## Slide 2: Bits
a bit is a binary digit that can have two possible values
can be physically represented with a two state device

## Slide 3: Bits

## Slide 4: Storing bits
Static random access memory (SRAM): stores each bit of data in a flip-flop, a circuit with two stable states
Dynamic Memory (DRAM): stores each bit of data in a capacitor, which stores energy in an electric field (or not)
Magnetic Disk: regions of the platter are magnetized with either N-S polarity or S-N polarity
Optical Disk: stores bits as tiny indentations (pits) or not (lands) that reflect light differently
Flash Disk: electrons are stored in one of two gates separated by oxide layers

## Slide 5: Binary Numbers
4211
1011

## Slide 6: Exercise
What (decimal) numbers are represented by the following (binary) values
  101111
  110011
  11111100011

## Slide 7: Binary Numbers

## Slide 8: ASCII characters

## Slide 9: Program Instructions
Python Code
def example1(n):
x = n + 1
return x
Binary Representation
10001101 01000111 00000001
11000011
Notes: leal 1(%rdi), %eax
retq

## Slide 10: Bits Require Interpretation
01000011 01010011 00110101 00110001
might be interpreted as
  The integer 112952657710
  A floating point number close to 211.207779
  The string “CS51”
  A portion of an image or video
  A portion of code
  An address in memory

## Slide 11: Information is Bits + Context

## Slide 12: Memory
101001011110101010101010111010101010101010000111110101010101011101010101011101010101011010101010101011101010010000000011010101111101010101010101010111010101011101010001010100000111100011101010111101010110100000110011101110110010000111010101011110001100110101000110000010101011001110011101011110110101
memory is a sequence of bytes
different "sections" of memory are used for different purposes
code section stores your programs
the stack is used to store variables to keep track of functions
The Stack
code

## Slide 13: Stack Frames
each time a function is called, that function call gets its own section of the stack, known as a stack frame or function frame
function name
instruction counter
parameter variables
local variables
return value
draw variables as named boxes
line number of next statement in the function body to execute
initially first line of body

## Slide 14: Example
ERASE WHOLE FRAME
def add_one(n):
x = n + 1
return x
num = add_one(46)
add_one
1
n
return
46
None
x
47
2
X
47
num
47

## Slide 15: Exercise
def foo(a, b):
x = a + b
y = 2 * b
return 2 * x + y
foo(2, 3)

## Slide 16: Control Flow and Nested Functions
def square(n):
if n <= 0:
return 0
else:
return n**2
def sum_squares(n):
sum = 0
for i in range(n):
sum += square(i)
return sum
sum_squares(2)

## Slide 17: Exercise
get_pos_int()
assume user enters
  hello
  47
def is_pos_int(s):
if str.isdigit(s):
return int(s) > 0
else:
return False
def get_pos_int():
done = False
while not Done:
s = input()
done = is_pos_int(s)
return s

## Slide 18: Global Variables
fav = 13
def good_choice(num):
b = (num == fav)
return b
good_choice
2
num
return
47
None
fav
13
b
False
global variables are outside of any stack frame. They are in a different section of memory!

## Slide 19: Scope
Storing a value in a variable:
  If there is a variable with that name in the current function's stack frame, store the value in that variable
  Otherwise create a new variable in the current function's stack frame and store the value there
Using a variable
  Check for a local variable with that name. If it exists, use the value stored in that variable
  Else if there exists a global variable with that name, use the value stored in that global variable
  Otherwise get a NameError
fav = 13
def good_choice(num):
b = (num == fav)
return b
def main():
in_str = input()
fav = int(in_str)
if good_choice(fav):
print("yay")
else:
print("boo")
Notes: note: shadowing
if comment out fav def the global!
try print in_str and b in opposite functions (will fail)

## Slide 20: Exercise
def print_example(s4,s5):
s1 = 3*s4
s2 = s4+s5
print(s1)
print(s2)
return s1+s2
s1 = '!'
s2 = '?'
print(s1)
s3 = print_example(s1,s2) print(s2)
print(s3)
print(s4)